# sound modes

# fx modes

# video modes

# paddle controllers

# secondary sid chip

# sid hex editor
Use RUNSTOP+F1 to enter normal SID HEX editing mode. This allows you to edit SID registers directly. Use 0-9 and A-F to enter the two digit address to change, followed by the two digit value to write to that address. If you are using the piano keyboard overlay, the numbers and some letters will be covered, so to use an alternate keyboard setup for the SID HEX edit: press RUNSTOP+F7 and then use the black keys for 0-9 and the center white keys for A-F.

INCLUDE SID REFERENCE CHART?

Cynthcart copyright 2016 paul slocum / www.qotile.net
# cynthcart v1.5.2
Cynthcart is a cartridge for the Commodore 64/128 that turns the computer into a standalone analog synthesizer. Cynthcart's key-command user interface allows it to be played and controlled without a monitor, making it especially suitable for live performance. The original Commodore 64 piano keyboard overlay can be used (illustrated above) and DATEL-compatible MIDI interface cartridges are now supported.
# features
+ 22 preset patches
+ Arpeggiator, portamento, vibrato, tremolo
+ Analog filter live control and effects
+ Mono stack, 3-voice mode, and 6-voice mode (with second SID)
+ Control of attack, release, and other sound parameters
+ MIDI support including pitch bend, patch changes, and controllers
+ On-screen help
+ Color visualizer display
+ SID hex editor for advanced users
+ Ability to turn off video chip to reduce noise
+ PAL and NTSC pitch tables with automatic selection
+ Copies itself to RAM (cartridge can be removed after loading)
# supported accessories
+ Commodore 64 piano keyboard overlay
+ DATEL and Kerberos MIDI interface cartridges
+ Paddle controllers for pulse width, vibrato, and pitch (use port 2)
+ 2nd SID chip at $DF00 (stereo chorus and 6-channel mode)

# keyboard controls
Most of the top two rows of the Commodore's keys function as a piano keyboard and are configured to be compatible with the piano keyboard overlay that was produced in the 80s. The top row is the black piano keys and the QWERTY row is the white piano keys. Notes can be locked down using the SHIFT LOCK button. The Commodore's other keys are used to select patches and change settings as indicated in the following tables.

KEY	by itself	with SHIFT	with CTRL
A	filter bass (#10)	Note Attack = 0	Note Release = 0
S	sweep arp (#11)	Note Attack = 5	Note Release = 5
D	pluck arp (#12)	Note Attack = 8	Note Release = 8
F	slow arp (#13)	Video Pattern 1	Poly Mode (default)
G	filter stack 1 (#14)	Video Pattern 2	5ths Mode
H	filter stack 2 (#15)	Video Pattern 3	5ths Port Mode
J	pulsar (#16)	Video On	Mono1 Mode
K	vibrato lead (#17)	Video on Sound	Arp1 Mode
L	slow rise (#18)	Video Off	Arp2 Mode
:	bend echo (#19)	Full Screen On	Arp3 Mode
;	arp lead (#20)	Full Screen Off	Arp4 Mode
=	6-voice saw (#21)		Arp5 Mode
RETURN	Help Page	Clear Modulation	6-Channel Mode
Z	saw bass (#0)	Tremolo Speed=0	Effects Off
X	gritty bass (#1)	Tremolo Speed=1	Filter Effects 1
C	portamento 5th (#2)	Tremolo Speed=2	Filter Effects 2
V	saw portamnto (#3)	Tremolo Speed=3	Filter Effects 3
B	pulse 5th (#4)	Tremolo Level=0	Filter Effects 4
N	pulse high (#5)	Tremolo Level=1	Filter Effects 5
M	triangle hi/lo (#6)	Tremolo Level=2	Pulse Effects 1
,	triangle drop (#7)	Tremolo Level=3	Pulse Effects 2
.	sid explosion (#8)		Pulse Effects 3
/	mute (#9)
cursor up/down	5ths Mode Off	Paddle 1 Off
cursor left/right	5ths Mode On	Paddle 1 On
SPACE	Bend Pitch
F1	Octave Highest	Portamento = 3	Volume = 9
F3	Octave High	Portamento = 2	Volume = 6
F5	Octave Low	Portamento = 1	Volume = 4
F7	Octave Lowest	Portamento Off	Volume = 0
backarrow	Custom Patch

KEY	with C= key	with RUNSTOP
A	Filter Cutoff = 0	Tuning = -40
S	Filter Cutoff = 1	Tuning = -30
D	Filter Cutoff = 2	Tuning = -20
F	Filter Cutoff = 3	Tuning = -10
G	Filter Cutoff = 4	Tuning = 0
H	Filter Cutoff = 5	Tuning = +10
J	Filter Cutoff = 6	Tuning = +20
K	Filter Cutoff = 7	Tuning = +30
L		Tuning = +40
Z	Filter On	Tuning = +50
X	Filter Off
C	Filter Disabled
V	Paddle 2 = Off
B	Paddle 2 = Pulse Width
N	Paddle 2 = LFO Speed
M	Paddle 2 = Pitch Bend
,	MIDI channel = omni
.	MIDI channel = 1
/	MIDI channel = 5
F1		Open SID Editor (keyboard)
F3		SID Editor Save
F7		Open SID Editor (piano)

# midi control
Cynthcart supports MIDI input through a DATEL or Kerberos MIDI interface cartridge. It responds to note data, patch changes, pitch bend, and various controllers. By default Cynthcart listens on all MIDI channels (omni mode) but single channels can also be selected. MIDI patch numbers are listed in the keyboard chart beside the patch names, and the chart below lists the Cynthcart MIDI controller numbers.

CC#	Parameter	CC#	Parameter
0	Filter Resonance	7	Volume
1 (wheel)	Filter Cutoff	8	Tremolo Depth
2	Choose Mode	9	Tremolo Speed
3	Choose FX Mode	13	Osc Waveform (all voices)
4	Attack	14	Osc Waveform (voice 2 only)
5	Release	15	Osc Waveform (voice 3 only)
6	Pulse Width